# DK9MBS Ham Rotor 3D

# Firmware
## Konzeption
### Statemachine

### Quellcode

https://github.com/dk9mbs/Rotor/tree/dev/fw-8266-arduino

## Technische Dokumentation

### Verfügbare GPIO Pin‘s
GPIO	Function	State	Einschränkungen
0	Boot mode select	3.3V	No Hi-Z
1	TX0	-	Not usable during Serial transmission
2	Boot mode select TX1	3.3V (boot only)	Don’t connect to ground at boot time Sends debug data at boot time
3	RX0	-	Not usable during Serial transmission
4	SDA (I²C)	-	-
5	SCL (I²C)	-	-
6-11	Flash connection	x	Not usable, and not broken out
12	MISO (SPI)	-	-
13	MOSI (SPI)	-	-
14	SCK (SPI)	-	-
15	SS (SPI)	0V	Pull-up resistor not usable
16	Wake up from sleep	-	No pull-up resistor, but pull-down instead Should be connected to RST to wake up

Quelle: https://tttapa.github.io/ESP8266/Chap04%20-%20Microcontroller.html

### Verwendung der ESP8266 Pins für den DK9MBS Rotor
Pin	Verwendung	Bemerkung
12	8825 Step
13	8825 Dir
14	8825 enabled
4	SW1	10K Pulldown
5	SW2
2	Endschalter	4,7K Pullup Schließer

### Pinbelegung NodeMCU mit ESP8266

### Pinbelegung DRV8825 Motor Treiber

M0	M1	M2	Schritt Auflösung	Anzahl Schritte für eine Umdrehung
0	0	0	1	200
1	0	0	1/2	400
0	1	0	1/4	800
1	1	0	1/8	1600
0	0	1	1/16	3200
1	0	1	1/32	6400

### LCD Display
Ein Display ist zur Zeit aus Ermangelung von freien GPIO Pins nicht vergesehen. Geplant ist hier ein I2C IO Expander der gemeinsam mit dem Display an einem Bus angeschlossen wird.